## Slide 1: 협동과제(경성대) : 한국형 상향식 S/W시스템 개발 - BufEEE Manual v0.5 (Bottom-up model for Energy, Emission and Evaluation)
기후변화대응 환경기술개발사업
연구단 : 한국형 상·하향식 온실가스 통합 감축 시스템 개발
경성대학교, 김후곤(hkim@ks.ac.kr)

## Slide 2
1. A Simplified Mathematical Formulation for BufEEE

## Slide 3: Overview : base year, model year, historic capacity, decision variable
2014(base year)
2015(first model year)
2050(last model year)
2013
2006
historic capacity
2020
2029
2023
2024
2007
2016
2016
2025
2041
new car production
2051(terminal year)
2049
2050

## Slide 4: RES example : transportation
car energy
oil(1)
electricity(3)
bio ethanol(2)
car energy
blended energy
gasoline+bio ethanol(4)
blended energy
car demand
2,000 billion km/year(5)
1 liter
1 liter
1kWh
1 liter
15km
1 liter
10KWh
1 liter
9/10 litter
100km
3KWh
50km
plug-in hybrid
6
middle car
5
electric car
7
BE
4
electricity
carrier
3
bio ethanol
carrier
2
oil carrier
1
energy tech
process tech
demand tech
1/9 litter
RES(Reference Energy System) denotes energy flows to satisfy a given demand

## Slide 5: RES example : normalization
car energy
oil(1)
electricity(3)
bio ethanol(2)
car energy
blended energy
gasoline+bio ethanol(4)
blended energy
1 liter
1 liter
1kWh
10/9
15km
1 liter
1KWh
1 liter
1
10km
3KWh
50km
plug-in hybrid
6
middle car
5
electric car
7
BE
4
electricity
carrier
3
bio ethanol
carrier
2
oil carrier
1
energy tech
process tech
demand tech
10/81
Set main input parameter to 1
car demand
2,000 billion km/year(5)

## Slide 6: RES example : parameters(inventory data)
car energy
oil(1)
electricity(3)
bio ethanol(2)
car energy
blended energy
gasoline+bio ethanol(4)
blended energy
car demand
2,000 billion km/year(5)
1 liter
1 liter
1kWh
10/9
15km
1 liter
1KWh
1 liter
1
10km
3KWh
50km
plug-in hybrid
6
middle car
5
electric car
7
BE
4
electricity
carrier
3
bio ethanol
carrier
2
oil carrier
1
energy tech
process tech
demand tech
  : the capacity variable of technology at time
  : the activity variable of technology at time
10/81
general parameter : model period, discount rate, etc.
costs : investment cost, fixed O&M cost, variable cost
historic capacity, lifetime, first year, last year, availablility factor, etc.
decision variables

## Slide 7: LP formulation : notations
Notations
  : model years
  : technology set
  : energy form set
  : demand set
  : the lifetime
  : historic capacity
  : main output efficiency of technology at time t  main output efficiency
  : sum of available historic capacities at
  : the activity variable of technology at time  main input unit(TOE)
  : the capacity variable of technology at time  main output unit(TOE or km)
tech(i)
1/9
30
1
main input
20
main output
By LP, all inputs and outputs satisfy proportionality. Thus we set main input as 1.
main output unit
inputs :
other input
other output
: outputs

## Slide 8: LP formulation : flow conservation/demand constraint
Let be the set of all energy forms. For an energy form , denotes the set of input technologies generating and denotes the set of technologies consuming . The energy flow balance constraint for can be written as
where is the energy flow of technology generating and is the energy flow of technology consuming .
Note that the main output of technology corresponds to where j is the generated by main output of technology i.
Let be the set of all service demands. Then, the demand constraint for the service demand can be expressed as
where is the required amount of service demand at time

## Slide 9: LP formulation : Objective Function
: the annualized investment cost for technology at time
  * 는 salvage cost를 고려하기 위한 것
: the fixed O&M cost per year for technology at time
: the variable cost per main output for technology at time
: the discount rate
Summing up these costs, the cost incurred by technology at time can be written as
- Note that is an amount of main output per main input, thus the variable cost must be .
- If you have a variable cost for main input, i.e , then you change as

## Slide 10: LP formulation : (Basic LP)
(Basic LP) | Minimize |  | 
 | Subjec to |  | 
(Basic LP) | Minimize |  | 
 | Subjec to |  | 
a very simple and minimal formulation with and
기존 formulation은 매우 복잡하며, 모든 경우를 다 포함한 것에서 출발함 (Basic LP)에서 출발하여, 복잡한 경우를 수용할 계획임
total available capacity : new capacity plus historic capacity for technology at time
Let introduce two dummy variables for convenience
a main output per main input for technology at time

## Slide 11: LP formulation : (Basic LP)
(Basic LP) | minimize |  | 
 | subjec to |  | 
(Basic LP) | minimize |  | 
 | subjec to |  | 
Let .
이면, 최적해에서 가 되면 되므로, capacity constraint는 redundant 함.
total available capacity : new capacity plus historic capacity for technology at time
Let introduce two dummy variables for convenience
a main output per main input for technology at time

## Slide 12: LP formulation : (Basic LP) example
car energy
oil(1)
electricity(3)
bio ethanol(2)
car energy
blended energy
gasoline+bio ethanol(4)
blended energy
car demand
2,000 billion km/year(5)
1 liter
1 liter
1kWh
10/9
15km
1 liter
1KWh
1 liter
1
10km
3KWh
50km
plug-in hybrid
6
middle car
5
electric car
7
BE
4
electricity
carrier
3
bio ethanol
carrier
2
oil carrier
1
10/81

## Slide 13: LP formulation : technology with vintage
vintage : the units’ respective dates of entry
생산년도 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
2011 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 |  |  |  |  | 
2012 |  | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  |  |  | 
2013 |  |  | 17 | 17 | 17 | 17 | 17 | 17 | 17 | 17 | 17 | 17 |  |  | 
2020 |  |  |  |  |  |  |  |  |  | 20 | 20 | 20 | 20 | 20 | 20
생산년도 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
2011 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 |  |  |  |  | 
2012 |  | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 |  |  |  | 
2013 |  |  | 17 | 17 | 17 | 17 | 17 | 17 | 17 | 17 | 17 | 17 |  |  | 
2020 |  |  |  |  |  |  |  |  |  | 20 | 20 | 20 | 20 | 20 | 20
(예제) 다음과 같이 수명이 10년이고, 생산년도(vintage)에 따라 연비가 향상되는 경우
From
Let
Worst case analysis : 차량 수명이 10년이고, 매년 생산량이 D/10로 동일한 경우
Assume

## Slide 14: LP formulation : vintage notation
  : technologies with vintage
  : and main output generating
  : amount of main ouput for technology at time produced in
amount of main ouput for technology at time
amount of main input for technology at time

## Slide 15: LP formulation : vintage notation
  : technologies with vintage
  : and main output generating
  : amount of main ouput for technology at time produced in
1
2
3
={1,2}
amount of main ouput for technology at time
amount of main input for technology at time

## Slide 16: LP formulation : (Basic LP with vintage)
car energy
oil(1)
electricity(3)
bio ethanol(2)
car energy
blended energy
gasoline+bio ethanol(4)
blended energy
car demand
2,000 billion km/year(5)
1 liter
1 liter
1kWh
10/9
15km
1 liter
1KWh
1 liter
1
10km
3KWh
50km
plug-in hybrid
6
middle car
5
electric car
7
BE
4
electricity
carrier
3
bio ethanol
carrier
2
oil carrier
1
10/81

## Slide 17: LP formulation : (Basic LP vi) example
oil(1)
electricity(5)
bio ethanol(3)
car energy
blended energy
gasoline+bio ethanol(6)
blended energy
car demand
2,000 billion km/year(9)
1
1
1
1
12km
1KWh
1 liter
6/100
94/100
5km
middle car
8
electric car
bioEthanolMix
6
electricityT
5
bioEthanolT
3
oilT
1
10
1
dieselT
2
diesel(2)
1
bioDieselT
4
bio diesel(4)
diesel+bio diesel(7)
1
2/100
98/100
bioDieselMix
7
14km
SUV
11
1 liter
9.4KWh
44km
plug-in hybrid
9
1 litre of gasoline. = 34MJ. = 9.4kWh
1 liter

## Slide 18: LP formulation : (Basic LP vi) example - normalization
oil(1)
electricity(5)
bio ethanol(3)
car energy
blended energy
gasoline+bio ethanol(6)
blended energy
car demand
2,000 billion km/year(9)
1
1
1
100/94
12km
1liter
1 liter
6/94
1
5×9.4 km
middle car
8
electric car
bioEthanolMix
6
electricityT
5
bioEthanolT
3
oilT
1
10
1
dieselT
2
diesel(2)
1
bioDieselT
4
bio diesel(4)
diesel+bio diesel(7)
100/98
2/98
1
bioDieselMix
7
14km
SUV
11
1 liter
1 liter
44km
plug-in hybrid
9
1 litre of gasoline. = 34MJ. = 9.4kWh
1 liter

## Slide 19: LP formulation : tr with multiple activities
Some technologies have multiple activities
car energy
oil(1)
electricity(3)
bio ethanol(2)
car energy
blended energy
gasoline+bio ethanol(4)
blended energy
1
1
1
10/9
15km
1 liter
1KWh
1KWh
1 liter
10/81
1
10km
30km
3KWh
50km
city
highway
plug-in hybrid
6
1
middle car
5
electric car
7
BE
4
electricity
carrier
3
bio ethanol
carrier
2
oil carrier
1
energy tech
process tech
demand tech
car demand
2,000 billion km/year(5)
,
2

## Slide 20: LP formulation : (Basic LP ma)
minimize |  | 
subjec to |  | 
minimize |  | 
subjec to |  | 
  : technologies with multiple activities
  : activity set for
  ,
  For convenience, let
denotes the set of activities generating
denotes the set of activities consuming
: the activity variable for and at time
: the main output efficiency of activity variable for at time

## Slide 21: LP formulation : (Basic LP ma) example
car energy
oil(1)
electricity(3)
bio ethanol(2)
car energy
blended energy
gasoline+bio ethanol(4)
blended energy
car demand
2,000 billion km/year(5)
1
1
1
10/9
15km
1 liter
1KWh
1KWh
1 liter
10/81
1
10km
30km
3KWh
50km
city
highway
plug-in hybrid
middle car
5
electric car
BE
4
electricity
carrier
3
bio ethanol
carrier
2
oil carrier
1
6
1
7
2

## Slide 22: LP formulation : (Basic LP)를 이용한 ma 표현
gasoline+bio ethanol(4)
2,000 billion km/year(5)
1 liter
1KWh
30km
3KWh
50km
city
highway
plug-in hybrid
6
1
2
gasoline+bio ethanol(4)
2,000 billion km/year(6)
1 liter
1KWh
30km
3KWh
50km
city
activity
highway
activity
6.1
6.2
plug-in hybrid
capacity
6
1km
1km
plug-in km dummy(5)
Let
multiple activities를 가지는 경우 capacity와 개별 activity를 각각의 technology로 분리함.
위의 plug-in의 경우 아래와 같이 3개의 technology로 분리
이때 변동비는 [city activity(6.1)] 및 [highway activity(6.2)]에 대해서만 부과하고, 투자비 및 연간 고정비는 [plug-in hybrid capacity(6)]에 부과함
(Basic LP)를 이용하여 ma를 표현할 수 있으므로, formulation의 단순화/일관성을 유지할 수 있고, 시스템 개발시에 UI 구현도 매우 단순화됨

## Slide 23: LP formulation : (Basic LP ma) example
car energy
oil(1)
electricity(3)
bio ethanol(2)
car energy
blended energy
gasoline+bio ethanol(4)
blended energy
car demand
2,000 billion km/year(6)
1
1
1
10/9
15km
1KWh
1 liter
10/81
1
10km
30km
50km
middle car
5
electric car
BE
4
electricity
carrier
3
bio ethanol
carrier
2
oil carrier
1
7
1KWh
city
activity
highway
activity
6.1
6.2
plug-in hybrid
capacity
6
1km
1km
plug-in km dummy(5)
dummy
1 liter
3KWh

## Slide 24: LP formulation : vi with aging(optional)
  Lithium Ion Battery degradation by aging
  ICE efficiency degradation by aging
aging |  |  |  | 
rate() | 1 | 0.98 |  | 0.82
aging |  |  |  | 
 | 1 | 0.98 |  | 0.82
1

## Slide 25: User Defined Constraint(UC) : decision variable
UC 의사결정 변수의 분류 : activity/capacity
  activity 제약식
    input 제약식 :
    output 제약식 :
  capacity 제약식 (for )
    new capacity 제약식 :
    total capacity 제약식 :

## Slide 26: User Defined Constraint(UC) : type1, type2, type3
UC 제약식의 범주
  연도별 제약식(type1, yearly constraint)
    가 된다. 예로는 emission, budget, market share, efficiency improvement, 기술대체 등을 들 수 있다.
  연도별 누적 제약식(type2, cumulative constraint) : 에 대하여
    가 된다. 예로는 누적 emission 제약, 예산 제약 등을 들 수 있다.
  시계열 제약(type3, time series constraint) : 와 에 대하여
      production smoothing 제약 등을 들 수 있다.
Dummy variable set :
dummy variable을 포함하도록 세가지 범주의 제약식을 수정하는데, 예를 들어 에 대한 yearly constraint는 및 에 대해

## Slide 27: UC : all possible constraints with dummies
UC make all possible constraints with dummy variables
a combined constraint
  (type1, ) + (type2, ) + (type3, )
Property : 의사결정변수 , , , 및 , 를 이용하여 만들어지는 (type1), (type2), (type3) 제약식을 이용하면, 모든 가능한 uc를 나타낼 수 있다.
목적함수의 변형

## Slide 28
2. BufEEE Systems

## Slide 29: 시스템개발 : 상향식 SW 시스템 개발 방향
Easy
Simple
Simplified Notation
Simplified LP Formulation
Worldwide
Simple, Easy and Worldwide(Open Project)
Easy Understandable
Easy UI
Open Web Site
Freeware

## Slide 30: System Development : new framework
Model(Basic LP all)
: activity variable
support
technology with vintage
technology with multiple activities
load region
Decision Variable()
: main output
: capacity variable
: total capacity variable
User Defined Constraint
yearly
cumulative
time series
RES
capacity constraint
energy flow conservation constraint
demand constraint
: dummy variable(
: dummy variable
Based on a new closed framework for bottom-up system development
  a simplified notation
  a new mathematical formulation
  only 3 constraints for user defined constraint
  9 possible outputs for optimal solution

## Slide 31: System Development : model/data/solution separation
Model(Basic LP all)
activity :(input)/(output)
support
technology with vintage
technology with multiple activities
load region
Decision Variable
capacity : (new)/(total)
User Defined Constraint
yearly
cumulative
time series
RES
capacity constraint
energy flow conservation constraint
demand constraint
dummy : ()/
()
Model/Data
Separation
Data(time series/historic)
support
require

## Slide 32: System Development : 3 BufEEE Systems
Data(time series/historic)
support
require
Model(Basic LP)
Model/Data
Separation
Solution
- decision variables
- dummy variables
- UC
type-1 :
type-2 :
type-3 :
get optimal
generate
solution
(Model/Data)/Solution
Separation

## Slide 33: System Development : 3 BufEEE Systems
Data(time series/historic)
support
require
Model(Basic LP)
Model/Data
Separation
GAMS BufEEE
Model(tr_model.gms)
Data(tr_data.gms)
Result(tr_result.gms)
EXCEL BufEEE
Model(RES sheet)
Data(ts sheet)
Result(sol sheet)
Web BufEEE
Model(res4.php)
Data(data.xlsx!ts)
Result(sol.xlsx!sol)
3BufEEE(Bottom-up model for Energy, Emission and Evaluation) Systems
lpsolve
glpk
cplex

## Slide 34
2.1 GAMS BufEEE

## Slide 35: GAMS BufEEE
Data(tr_data_vi.gms)
$onempty
Sets
I technologies / 1*7/
J energy-forms /1*5/ ;
Parameters
a(i) /1 100, 2 110, .../
Tables d(i,j)
....
Scalar f /10/;
Decoupling of Model/Data : GAMS supports it by using $onmulti
a GAMS code for a large scale problem decouples data, model, and output
Model(tr_model_vi.gms)
$onmulti
$onempty
Sets
I(*) technologies / /
J(*) energy-forms / / ;
Parameters
a(i) / /;
Tables d(i,j) / /;
Scalar f / na /;
Variables x(i,j), z
Equations
....
Balance(j).. sum(j,x(i,j)) =g= a(i)
Model tr /all/;
tr.optfile=1;
solve tr using lp minimizing z;
Output(tr_result.gms)
$onmulti
$onempty
Display x.l, x.m ;
run(tr_khg.gms)
$include tr_data_vi.gms
$include tr_model_vi.gms
$include tr_output.gms
LP gen(cplex.opt)
writelp tr_khg.lp

## Slide 36: LP formulation : (Basic LP vi)
minimize |  | 
subjec to |  | 
minimize |  | 
subjec to |  | 
: P_V(j,i)
: I_v(i)
tr_model_vi.gms
: hminus(i,s)
Variables
: x(i,t)
: X_out(i,t)
: x_vi(i,s,t)
: y(i,t)
: Y_cap(i,t)
where
: l_max
capacity(i,t)
capacity_vi_hist(i,s,t,prevT)
capacity_vi_new(i,s,t,tt)
flow_conservation(j,t)
demand(j,t)
Y_cap_dummy(i,t)
X_out_dummy(i,t)
X_out_vi_dummy(i,t)
x_sum_vi_dummy(i,t)
y_zero(i,t)

## Slide 37: (Basic LP vi) gams coding
tr_model_vi.gms
S(*) superset of T including historic years and time periods / pr2006*pr2014, 1*36 /
T(s) time periods /1*36 /
I(*) technologies / /
I_0(i) technologies with no cap. constraint / 1*7 /
I_v(i) technologies with vintage / 8, 9, 10,11 /
prevT(s) / pr2006*pr2014 /
capacity_vi_hist(i,t,s)$(I_v(i) and t.val<life(i) and (ord(t)-life(i)+1+(l_max-1))<=ord(s) and ord(s)<l_max)..
eff_prev(i,s)*x_vi(i,s,t) =l= hminus(i,s) ;
x_vi(i,s,t):
y(i,t) :
eff(i,t) :
eff_prev(i,s) :
hminus(i,s) :

## Slide 38: (Basic LP vi) gams coding
tr_model_vi.gms
S(*) superset of T including historic years and time periods / pr2006*pr2014, 1*36 /
T(s) time periods /1*36 /
I(*) technologies / /
I_0(i) technologies with no cap. constraint / 1*7 /
I_v(i) technologies with vintage / 8, 9, 10,11 /
capacity_vi_new(i,s,t,tt)$(I_v(i) and (ord(s)+(l_max-life(i)))>=life(i) and ord(tt)=((ord(s)-(l_max-life(i)))-(life(i)-1))
and ord(t)>=((ord(s)-(l_max-life(i)))-(life(i)-1)) and ord(t)<=(ord(s)-(l_max-life(i))) )..
eff(i,tt)*x_vi(i,s,t) =l= y(i,tt) ;
x_vi(i,s,t):
y(i,t) :
eff(i,t) :

## Slide 39: (Basic LP vi) gams coding
tr_model_vi.gms
S(*) superset of T including historic years and time periods / pr2006*pr2014, 1*36 /
T(s) time periods /1*36 /
I(*) technologies / /
I_0(i) technologies with no cap. constraint / 1*7 /
I_v(i) technologies with vintage / 8, 9, 10,11 /
x_vi(i,s,t):
y(i,t) :
eff(i,t) :
X_out(i,t) :
X_out_dummy(i,t )$(not I_v(i))..
X_out(i,t) =e= eff(i,t)*x(i,t);
X_out_vi_dummy(i,t)$(I_v(i))..
X_out(i,t) =e= sum(s$( ord(s)>=(ord(t)-life(i)+1+(l_max-1)) and ord(s)<l_max), eff_prev(i,s)*x_vi(i,s,t) )
+sum(s$( ((ord(s)-l_max+1)>=1 and (ord(s)-l_max+1)>=ord(t)-life(i)+1) and (ord(s)-l_max+1)<=ord(t) ), eff(i,s)*x_vi(i,s,t)) ;

## Slide 40: (Basic LP vi) gams coding
tr_model_vi.gms
S(*) superset of T including historic years and time periods / pr2006*pr2014, 1*36 /
T(s) time periods /1*36 /
I(*) technologies / /
I_0(i) technologies with no cap. constraint / 1*7 /
I_v(i) technologies with vintage / 8, 9, 10,11 /
x_vi(i,s,t):
y(i,t) :
eff(i,t) :
X_out(i,t) :
x_sum_vi_dummy(i,t)$(I_v(i))..
x(i,t) =e= sum(s$( ord(s)>=(ord(t)-life(i)+1+(l_max-1)) and ord(s)<l_max), x_vi(i,s,t) )
+sum(s$( ((ord(s)-l_max+1)>=1 and (ord(s)-l_max+1)>=ord(t)-life(i)+1) and (ord(s)-l_max+1)<=ord(t) ), x_vi(i,s,t)) ;

## Slide 41: (Basic LP vi) gams coding
tr_model_vi.gms
S(*) superset of T including historic years and time periods / pr2006*pr2014, 1*36 /
T(s) time periods /1*36 /
I(*) technologies / /
I_0(i) technologies with no cap. constraint / 1*7 /
I_v(i) technologies with vintage / 8, 9, 10,11 /
C(j,i)
P(j,i)
P_V(j,i)
flow_conservation(j,t)$(not K(j))..
sum(P_V(j,i), X(i,t)) + sum(P(j,i)$(not P_V(j,i)), Pro(j,i,t) * x(i,t))=g= sum(C(j,i),Cons(j,i,t) * x(i,t));
demand(j,t)$(K(j))..
sum(P_V(j,i), X(i,t)) + sum(P(j,i)$(not P_V(j,i)), Pro(j,i,t) * x(i,t)) =g= dem(j,t);

## Slide 42: UC (type1, yearly constraint)의 GAMS 구현
Constraint type(C_type) : (T1, yearly), (T2, cumulative), (T3, time series)
UC decision variable type(V_type) : (actInp), (actOut), (newCap), (totalCap)
dummy variables(D1, D2) : (D1), (D2)
Inequality type(EQ1) : (geq), (eq), (leq)
Possible UC combinations : C_type(3) variables(4) EQ1(3) =36 types
  GAMS does not support an inequality type selection operator
  GAMS does not support a variable selection operator
Example : type1(yearly), (actInp), (geq)
we make a combined constraint including all four activity/capacity variables with the following deltas(a variable selection operator)
With , we can reduce UCs to 9 types for GAMS : C_type(3) EQ1(3) = 9 types

## Slide 43: UC (type1, yearly constraint)의 GAMS 구현
t1_geq(t123,C_type,EQ1,t) t1_geq(t123,C_type,EQ1,t)$(uc_info(t123,C_type,EQ1) and sameas(C_type,'yearly') and sameas(EQ1,'geq'))..
sum(i, uc_I_param(t123,i,t)*x(i,t)) * delta(t123,'actInp')
+sum(i, uc_I_param(t123,i,t)*X_out(i,t)) * delta(t123,'actOut')
+sum(i, uc_I_param(t123,i,t)*y(i,t)) * delta(t123,'newCap')
+sum(i, uc_I_param(t123,i,t)*Y_cap(i,t)) * delta(t123,'totalCap')
+sum(d1,uc_d1_param(t123,d1,t)*v(d1,t)) +sum(d2,uc_d2_param(t123,d2)*w(d2)) =g= RHS(t123,t);
t1_eq(t123,C_type,EQ1,t) t1_geq(t123,C_type,EQ1,t)$(uc_info(t123,C_type,EQ1) and sameas(C_type,'yearly') and sameas(EQ1,'eq'))..
t1_geq(t123,C_type,EQ1,t) t1_geq(t123,C_type,EQ1,t)$(uc_info(t123,C_type,EQ1) and sameas(C_type,'yearly') and sameas(EQ1,‘leq'))..
Sets
D1 dummy variables with time series / v1, v2, z1, z2, u1, u2, u3, u4 /
D2 dummy variables without time series / w1 /
EQ1 equation eqaulity /geq, eq, leq /
C_type constraint types / yearly, cumul, ts /
V_type constraint variable types / actInp, actOut, newCap, totalCap /
T1(*) yearly constraint - type1 / 1 "y_prod_total", 2 "y_denominator", 3 "test11" /
T2(*) cumulative constraint - type2 / 4 "test4_cumul" /
T3(*) time series constraint - type3 / 5 "ICE_ts" /
T123(*) / Set.T1, Set.T2, Set.T3 /
uc_info(t123, C_type, EQ1) / 1.yearly.eq, 2.yearly.eq, 3.yearly.eq, 4.cumul.geq, 5.ts.leq /
Table delta(t123, V_type)
actInp actOut newCap totalCap
1 0 0 1 0
2 0 0 1 0
3 0 0 1 0
4 1 0 0 0
5 0 0 1 0
Table uc_I_param(t123,i,t)
1 2
1.5 1 1
1.6 1 1
1.7 1 1
2.5 0.083 0.083
2.6 0.018 0.018
2.7 0.021 0.021
4.5 1 1
Variables
v(d1,t) :
w(d2) :
Table uc_d1_param(t123,d1,t)
1 2
1.v1 -1 -1
2.v2 -1 -1
3.u1 -1 -1
4.u3 -1 -1
Parameters uc_d2_param(t123,d2) / 3.w1 1 /;

## Slide 44: UC (type2, cumulative constraint)의 GAMS 구현
Example : type2(cumulative), (actInp), (geq)
we make a combined constraint including all four activity/capacity variables with the following deltas(a variable selection operator)
t2_geq(t123,C_type,EQ1,t) t1_geq(t123,C_type,EQ1,t)$(uc_info(t123,C_type,EQ1) and sameas(C_type,'cumul') and sameas(EQ1,'geq'))..
sum(i, sum(tt$(tt.val<=t.val), uc_I_param(t123,i,tt)*x(i,tt)))*delta(t123,'actInp')
+sum(i, sum(tt$(tt.val<=t.val), uc_I_param(t123,i,tt)*X_out(i,tt)))*delta(t123,'actOut')
+sum(i, sum(tt$(tt.val<=t.val), uc_I_param(t123,i,tt)*y(i,tt)))*delta(t123,'newCap')
+sum(i, sum(tt$(tt.val<=t.val), uc_I_param(t123,i,tt)*Y_cap(i,tt)))*delta(t123,'totalCap')
+sum(d1,uc_d1_param(t123,d1,t)*v(d1,t)) +sum(d2,uc_d2_param(t123,d2)*w(d2)) =g= RHS(t123,t);
t2_eq(t123,C_type,EQ1,t) t1_geq(t123,C_type,EQ1,t)$(uc_info(t123,C_type,EQ1) and sameas(C_type,‘cumul') and sameas(EQ1,'eq'))..
t2_leq(t123,C_type,EQ1,t) t1_geq(t123,C_type,EQ1,t)$(uc_info(t123,C_type,EQ1) and sameas(C_type,‘cumul') and sameas(EQ1,‘leq'))..

## Slide 45: UC (type3, time series)의 GAMS 구현
Example : type3(time series), (actInp), (geq)
    dummy variable도 time series를 허용함
    에서 이면, 가 됨
Production Smoothing Constraint
Property 2. If then
    단종 시키는 시나리오를 반영할 수 있음
Production Smoothing
재고관리

## Slide 46: UC (type3, time series)의 GAMS 구현
  type3 equation id=5 :
fix_equations ts_equations | Set S_d1(t123, d1, past) /5.v5.2, 5.v5.1, 5.v5.0 /; Parameters S_d1_init(t123, d1, past,t) / 5.v5.2.1 30, 5.v5.1.1 29, 5.v5.2.2 29 /; Set fixed_t_i_var(t123, i, past, t) / 5.5.0.1, 5.5.1.2 5.5.0.2 /; Set fixed_t_d1_var(t123, d1, past, t) / 5.v5.0.1, 5.v5.1.2 5.v5.0.2 /;
 | Set past /0, Set.T/; Set fix_year(t123, t) /5.1, 5.2/; Set S_i(t123, i, past) /5.5.1, 5.5.0 /; Parameters S_i_init(t123, i, past,t) /5.5.0.1 50 /;
Table uc_t3_I_param(t123,i,past,t)
1 2 3
5.5.1 1 1 1
5.5.0 -1 -1 -1
Table uc_t3_d1_param(t123,d1,past,t)
1 2 3
5.v5.2 1 0.99 0.98
5.v5.1 -0.1 -0.1 -0.1
5.v5.0 1 1 1
T1(*) yearly constraint - type1 / 1 "y_prod_total", 2 "y_denominator", 3 "test11" /
T2(*) cumulative constraint - type2 / 4 "test4_cumul" /
T3(*) time series constraint - type3 / 5 "ICE_ts" /
T123(*) / Set.T1, Set.T2, Set.T3 /
uc_info(t123, C_type, EQ1) / 1.yearly.eq, 2.yearly.eq, 3.yearly.eq, 4.cumul.geq, 5.ts.leq /

## Slide 47: UC (type3, time series)의 GAMS 구현
  type3 equation id=5 :
fix_equations ts_equations | Set S_d1(t123, d1, past) /5.v5.2, 5.v5.1, 5.v5.0 /; Parameters S_d1_init(t123, d1, past,t) / 5.v5.2.1 30, 5.v5.1.1 29, 5.v5.2.2 29 /; Set fixed_t_i_var(t123, i, past, t) / 5.5.0.1, 5.5.1.2 5.5.0.2 /; Set fixed_t_d1_var(t123, d1, past, t) / 5.v5.0.1, 5.v5.1.2 5.v5.0.2 /;
 | Set past /0, Set.T/; Set fix_year(t123, t) /5.1, 5.2/; Set S_i(t123, i, past) /5.5.1, 5.5.0 /; Parameters S_i_init(t123, i, past,t) /5.5.0.1 100 /;
Table uc_t3_I_param(t123,i,past,t)
1 2 3
5.5.1 1 1 1
5.5.0 -1 -1 -1
Table uc_t3_d1_param(t123,d1,past,t)
1 2 3
5.u4.2 1 1 1
5.u4.1 -1 -1 -1
5.u4.0 1 1 1

## Slide 48: UC (type3, time series)의 GAMS 구현
Example : type(ts), (actInp), (geq)
we make a combined constraint including all four activity/capacity variables with the following deltas(a variable selection operator)
t3_geq_fix(t123,C_type,EQ1,t)$(uc_info(t123,C_type,EQ1) and sameas(C_type,'ts') and sameas(EQ1,'geq') and fix_year(t123,t))..
sum(i, sum(past$S_i(t123, i, past), uc_t3_I_param(t123,i,past,t)*S_i_init(t123,i,past,t)))
+ sum(i, sum(past$fixed_t_i_var(t123, i, past,t), uc_t3_I_param(t123,i,past,t)*x(i,t-past.val)))*delta(t123,'actInp')
+ sum(i, sum(past$fixed_t_i_var(t123, i, past,t), uc_t3_I_param(t123,i,past,t)*X_out(i,t-past.val)))*delta(t123,'actOut')
+ sum(i, sum(past$fixed_t_i_var(t123, i, past,t), uc_t3_I_param(t123,i,past,t)*y(i,t-past.val)))*delta(t123,'newCap')
+ sum(i, sum(past$fixed_t_i_var(t123, i, past,t), uc_t3_I_param(t123,i,past,t)*Y_cap(i,t-past.val)))*delta(t123,'totalCap')
+sum(d1, sum(past$S_d1(t123, d1, past), uc_t3_d1_param(t123,d1,past,t)*S_d1_init(t123,d1,past,t))
+ sum(past$fixed_t_d1_var(t123, d1, past,t), uc_t3_d1_param(t123,d1,past,t)*v(d1,t-past.val)) )
+sum(d2,uc_d2_param(t123,d2)*w(d2)) =g= RHS(t123,t);
t3_geq_ts(t123,C_type,EQ1,t)$(uc_info(t123,C_type,EQ1) and sameas(C_type,'ts') and sameas(EQ1,'geq') and not fix_year(t123,t))..
sum(i, sum(past$S_i(t123,i,past), uc_t3_I_param(t123,i,past,t)*X(i,t-past.val)))*delta(t123,'actInp')
+sum(i, sum(past$S_i(t123,i,past), uc_t3_I_param(t123,i,past,t)*X_out(i,t-past.val)))*delta(t123,'actOut')
+sum(i, sum(past$S_i(t123,i,past), uc_t3_I_param(t123,i,past,t)*y(i,t-past.val)))*delta(t123,'newCap')
+sum(i, sum(past$S_i(t123,i,past), uc_t3_I_param(t123,i,past,t)*Y_cap(i,t-past.val)))*delta(t123,'totalCap')
+sum(d1, sum(past$S_d1(t123,d1,past), uc_t3_d1_param(t123,d1,past,t)*v(d1,t-past.val)))
+sum(d2,uc_d2_param(t123,d2)*w(d2)) =g= RHS(t123,t);
t3_eq_fix(t123,C_type,EQ1,t)$(uc_info(t123,C_type,EQ1) and sameas(C_type,'ts') and sameas(EQ1,'eq') and fix_year(t123,t))..
t3_eq_ts(t123,C_type,EQ1,t)$(uc_info(t123,C_type,EQ1) and sameas(C_type,'ts') and sameas(EQ1,'eq') and not fix_year(t123,t))..
t3_leq_fix(t123,C_type,EQ1,t)$(uc_info(t123,C_type,EQ1) and sameas(C_type,'ts') and sameas(EQ1,‘leq') and fix_year(t123,t))..
t3_leq_ts(t123,C_type,EQ1,t)$(uc_info(t123,C_type,EQ1) and sameas(C_type,'ts') and sameas(EQ1,‘leq') and not fix_year(t123,t))..
Table delta(t123, V_type)
actInp actOut newCap totalCap
5 0 0 1 0

## Slide 49
2.2 Excel BufEEE

## Slide 50: Excel BufEEE :입력1
General 입력
Energy Levels/Forms 입력
2 VBA functions
= rg(range)  returns range address
=io(cell)  returns name(id) for energy form/technology

## Slide 51: Excel BufEEE :입력2
Technology 입력

## Slide 52: Excel BufEEE UI
RES sheet
ts sheet
Data(tr_data.gms)
$onempty
Sets
I technologies / 1*7/
J energy-forms /1*5/ ;
Parameters
a(i) /1 100, 2 110, .../
Tables d(i,j)
....
Scalar f /10/;
sol sheet

## Slide 53: lpsolve setup for EXCEL vba
다음 site에서 lpsolve IDE를 다운로드하여 설치하면, 설치된 folder에 lpsolve55.dll이 있음
  https://sourceforge.net/projects/lpsolve/files/latest/download?source=top3_dlp_t5
  윈도우 64bit인 경우 : c:\windows\SysWow64 에 lpsolve55.dll를 복사
  윈도우 32bit인 경우 : c:\windows\system32 에 lpsolve55.dll를 복사
http://cat.ks.ac.kr/pt/excelBufEEEpy.xlsm 을 download 받아서 실행하면 됨

## Slide 54: 제약식의 입력 : type 1(yearly)
평균 연비(CAFE) 제약식
평균 연비만 계산하기
  다음 두 제약식을 추가
    y_prod_total :
    y_denominator :
  “sol sheet”에서 를 계산하면 됨
Market Share
  MS_ICE_vs_SUV :
 | technology | 
constraint name | tech.(t_id) | ts
y_prod_total | ICE(8) | 1
 | PHEV(9) | 1
 | EV(10) | 1
 | SUV(11) | 1
 | v1(1) | -1
 | EQ | eq
 | RHS | 0
y_denominator | ICE(8) | ts!D59:AM59
 | PHEV(9) | ts!D60:AM60
 | EV(10) | ts!D61:AM61
 | SUV(11) | ts!D62:AM62
 | v2(2) | -1
 | EQ | eq
 | RHS | 0
MS_ICE_vs_SUV | ICE(8) | 0.5
 | SUV(11) | -0.5
 | EQ | geq
 | RHS | 0

## Slide 55: 제약식의 입력 : type 3(time series)
Production Smoothing : 기
  종방지/급격한 도입 제한
  ICE_ts
    ICE_ts _LB:
    ICE_ts_UB:
  SUV_ts
    SUV_ts_LB :
  EV_ts
    EV_ts_UB :
S_i | initial | ts
ICE_ts_LB | ICE(8) |  | -1 | 55 | 1
 |  |  | 0 |  | -1
 | EQ | leq |  |  | 
 | RHS | 10 | S_i | initial | ts
ICE_ts_UB | ICE(8) |  | -1 | 55 | 2
 |  |  | 0 |  | -1
 | EQ | geq |  |  | 
 | RHS | 0 | S_i | initial | ts
SUV_ts_LB | SUV(11) |  | -1 | 45 | 1
 |  |  | 0 |  | -1
 | EQ | leq |  |  | 
 | RHS | 5 | S_i | initial | ts
EV_ts_UB | EV(10) |  | -1 | 1 | 2
 |  |  | 0 |  | -1
 | EQ | geq |  |  | 
 | RHS | 0 |  |  | 

## Slide 56: 제약식의 입력 : type 3(time series)
Production Smoothing
  도입 제한
  new_EV_ts
    new_EV_ts _LB:
    new_EV_ts_UB :
    new_EV_t1_UB(type1) : starting value UB
S_i | initial | ts

## Slide 57: 제약식의 입력 : type 3(time series)
Production Smoothing , fyear
  fyear이후에 도입 가능/급격한 도입 제한
  new_FC_ts
    new_FC_start_year : first year is
    new_FC_ts _LB:
    new_FC_ts_UB :

## Slide 58
2.3 Web BufEEE
Under Construction
Web BufEEE(http://cat.ks.ac.kr/RES4/res.php)
Will be made with
Frontend
- HTML/CSS/javascript
- d3/KaTeX
Frontend
- python/Flask
- mongodb

## Slide 59: 시스템개발 : Web App 개발 개념도
LP generation
Reporting/Result Analysis
Browser(GUI)
MML : GAMS, AMPL, MathProg
LP file : MPS, LP
LP solver : glpk, CPLEX, Gurobi, COIN-OR
LP solver API
LP viewer : KaTax
Plot/Chart : HTML5 SVG/d3
Batch outputs
MySQL or
MongoDB
Language : HTML5/CSS/Javascript
RES 설계/구축
BAU/시나리오 구축
Variable 추가
Constraint 추가
Web viewer : HTML5/CSS/Javascript

## Slide 60: 시스템개발 : SW System/UI 개발 방법론
UI 구현
Web BufEEE RES/Dummy/Constraint 입출력
JSON
HTML5/CSS3/Javascript
for client
LP 구현/실행
LP API
glpk(LP Solver)
LP viewer
KaTeX
JSON : JavaScript Object Notation
HTML : HyperText Markup Language
CSS : Cascading Style Sheets
PHP for server
RES drawer
d3
Web BufEEE : http://cat.ks.ac.kr/RES4/res.php

## Slide 61: 시스템개발 : RES/에너지 폼 UI

## Slide 62: 시스템개발 : Dummy variable의 JSON 표현
Dummy variable set :
  dummy variable : for
  모든 제약식에 와 를 포함하도록 변형

## Slide 63: 시스템개발 : KaTeX를 통한 LP 수식의 구현

## Slide 64: 시스템개발 : d3를 이용한 output viewer구현

## Slide 65
3. GAMS-python-Excel 연동

## Slide 66: GAMS-python-Excel 연동
Excel(Data Provider)
Python(통합 환경제공)
xlwings
GAMS
GAMS(model/data)
tr_model_vi.gms
tr_data_vi.gms
Solver
- cplex ...
data generation for GAMS
data read/write
from Excel
GAMS-Python API
- read/run GAMS model
- get optimal from GAMS

## Slide 67: installs
python install : www.python.org
  C:\Python36>에 3.6.x 를 install
GAMS install
  www.gams.com : 2017.7.24 현재 24.8.5가 있음
  C:\GAMS\win64\24.8\apifiles\Python\api_36 이 있음(python 3.6을 위한 것)
  C:\GAMS\win64\24.8\apifiles\Python : transport1.py ~ transport14.py 등의 예제
  >cd C:\GAMS\win64\24.8\apifiles\Python\api_36
  >python setup.py install
  C:\GAMS\win64\24.8\apifiles\Python>python transport1.py 을 실행하면 됨.
jupyter install
  >pip3 install —upgrade pip  pip(python install package)
  >pip3 install jupyter
  >jupyter notebook

## Slide 68: excel에서 xlwings run
xlwings(v0.11) install
  >pip install xlwings 실행
  excel에 오른쪽과 같은 ribbon메뉴가 생김
  만약 ribbon 메뉴가 생기지 않으면
  >xlwings addin remove
  >xlwings addin install
  을 실행하고 다시 excel을 실행하면 ribbon메뉴가 생김
예제 파일 download
  (http://cat.ks.ac.kr/pt1/excelBufEEEpy.zip 을 download 하여,
  C:\excelBufEEEpy> 에 압축풀고 excelBufEEEpy.xlsm을 실행하면 됨)
직접 만들기
  C:\>xlwings quickstart excelBufEEEpy 실행
  excelBufEEEpy.py와 excelBufEEEpy.xlsm 이 생성됨
  - excelBufEEEpy.py에는 default로 오른쪽의 내용이 생성됨
  - excelBufEEEpy.xlsm에서 “Import Functions”를 실행함
  - A2셀에 “=hello(A1)” 을 실행하여
  “hello kim”이 나오면 됨
Required: Enable Trust access to the VBA project object model under
File >Options > Trust Center > Trust Center Settings > Macro Settings
 하위 version의 xlwings로 만든 excel 파일은 Migrate to v0.11 (Add-in) 참조하여 upgrade

## Slide 69: xlwings에서 function 및 sub 만들기
2. 엑셀에서 새로 만들어진 function 및 sub를 인식 시키기 위해, 다음 icon을 실행함
아래와 같이 @xw.func 및 @xw.sub 밑에 function 및 sub를 정의하면 됨
(@ 으로 시작하는 명령을 python에서는 decorator라고 함)
3. function은 sheet의 수식에서 실행하면 되고, sub는 개발도구-매크로에서 실행하면 됨
 function이나 sub가 정상작동되다가 이상할때 실행

## Slide 70: python과 GAMS의 연동
두가지 실행 방법이 있음
엑셀에서 function 및 sub로 실행하는 방법
python에서 __main__을 이용하여 실행하는 방법
from win32com.client import Dispatch
Python에서 Excel을 read/write 하는 library는 매우 다양하게 있음. 어떠한 것을 사용하여도 됨
pywin32
python library(xlwings, openpyxl, xlrd, xlwt, pandas, numpy 등)
GAMS python library function
pywin32를 이용하면 VBA 명령어를 fully 실행할 수 있지만, 다음을 download하고 실행하여야 함
https://sourceforge.net/projects/pywin32/files/pywin32/Build%20221/pywin32-221.win-amd64-py3.6.exe/download
예제
from win32com.client import Dispatch
.......
app_xl = Dispatch("Excel.Application")
wb = app_xl.ActiveWorkbook
RES = wb.Sheets('RES')
sht = wb.Sheets('Solution')
os.chdir(wb.Path)
print(wb.Path)
print(os.getcwd())
sht.Range('A1').value = 'aaa‘ # write to Excel

## Slide 71: python에서 sub를 이용하여 실행하는 방법(model/data separation)
엑셀에서 my_macro를 실행 하면 됨.

## Slide 72: LP formulation : (Basic LP vi)
minimize |  | 
subjec to |  | 
minimize |  | 
subjec to |  | 
: P_V(j,i)
: I_v(i)
tr_model_vi.gms
: hminus(i,prevT)
: x_vi(i,s,t)
where
: l_max
capacity(i,t)
capacity_vi_hist(i,s,t,prevT)
capacity_vi_new(i,s,t,tt)
flow_conservation(j,t)
demand(j,t)
Y_cap_dummy(i,t)
X_out_dummy(i,t)
X_out_vi_dummy(i,t)
x_sum_vi_dummy(i,t)
y_zero(i,t)

## Slide 73: python에서 __main__을 이용하여 실행하는 방법(model/data separation)
실행은 다음과 같이 하면됨.

## Slide 74: xlwings와 worksheet
import xlwings as xw
xw_wb = xw.Book.caller() # xw_wb = xw.Book(r'C:/excelPyEx/excelPyEx.xlsm')
RES = xw_wb.sheets['RES']
sht = xw.xw_wb.sheets['Solution’]
sht.clear_contents()
sht.range(‘B1').value=[1, 2, 3] # row orientation for list
sht.range(‘A2').value=[[10], [20], [30]] # column orientation for nested list

## Slide 75: xlwings와 GAMS python
from gams import *
xw_wb = xw.Book.caller()
os.chdir(xw_wb.api.path)
ws = GamsWorkspace(os.getcwd())
t2 = ws.add_job_from_file(os.path.join(os.getcwd(),"tr_model_vi.gms"))
opt = ws.add_options()
opt.optfile=1
opt.defines["incname"] = "tr_data_vi" # include “tr_data_vi.gms” for data
t2.run(gams_options=opt)
sht.range('A1').value = " Obj: {:,.2f}".format(t2.out_db["z"].find_record().level)
if (int(t2.out_db["modelstat"].find_record().value)==1):
modelstat="Optimal"
elif (int(t2.out_db["modelstat"].find_record().value)==4):
modelstat="Infeasible"
else:
modelstat="modelstat error"
tr_model_vi.gms
.......
Model tr /all/ ;
tr.optfile=1;
Solve tr using lp minimizing z ;
Scalar modelstat / /;
modelstat=tr.modelstat;
GAMS에서 정의한
set, parameter, table, scalar
variable 의 optimal solution
등은
t2.out_db[＂name"]
을 통해 접근할 수 있음

## Slide 76: GAMS model/data로 부터 python에서 읽어오기
from gams import *
....
t2.run(gams_options=opt)
.....
# GAMS set definition
# I technologies / 1 "gasolineC", 2 "dieselC", 3 "bio ethanolC", 4 "bio dieselC", .... /
I=[int(rec.key(0))-1 for rec in t2.out_db["I"]] # GAMS set name
tech_names=[rec.text for rec in t2.out_db["I"]] # GAMS set explanatory text
demand=np.zeros(tau)
x=np.zeros((noOfTechs,tau))
for rec in t2.out_db["dem"]: # GAMS parameter
demand[int(rec.key(1))-1]=rec.value
for rec in t2.out_db["x"]: # GAMS variable
x[int(rec.key(0))-1,int(rec.key(1))-1]=rec.level
I_0=[int(rec.key(0))-1 for rec in t2.out_db["I_0"]] # I /1*11/, I_0 /1*7/
y=np.zeros((noOfTechs,tau))
for rec in t2.out_db["y"]:
y[int(rec.key(0))-1,int(rec.key(1))-1]=rec.level
sht.range('B'+str(row)).value = np.delete(y, I_0, axis=0) # I_0 에 속한 row 들을 삭제함

## Slide 77: GAMS python에서 Excel에 write하기
import xlwings as xw
from gams import *
....
demand=np.zeros(tau)
x=np.zeros((noOfTechs,tau))
for rec in t2.out_db["dem"]: # GAMS parameter
demand[int(rec.key(1))-1]=rec.value
for rec in t2.out_db["x"]: # GAMS variable
x[int(rec.key(0))-1,int(rec.key(1))-1]=rec.level
row=4
sht.range('A'+str(row)).value='demand(km)’
sht.range('B'+str(row)).value=demand
row+=2
tech_names=[rec.text for rec in t2.out_db["I"]]
x_names=[['x['+tech+'('+str(index+1)+')]'] for index, tech in enumerate(tech_names)]
sht.range('A'+str(row)).value=x_names
sht.range('B'+str(row)).value = x